SUMA_MakeThresholdOutlines
- ado = SUMA_Overlay_OwnerADO(Sover);
- SO = (SUMA_SurfaceObject *)ado;
- Check that required pointers not NULL
- SUMA_Find_ColorMap
  - Ensure there are color maps. If not, exit.
  - Cycle through maps to find required map
  - If found, return map. Otherwise return failed to find map
- If colormap not found, return with error message.
- Create a scaled color vector
- If show mode Con or CaC
  - return = (SUMA_NeedsLinearizing(ColMap))
    - If there is no N_col x 1 vector containing the fraction of scale assigned to each color, (values shown on the right of the colorbar in AFNI) return 0
    - If number of colors in the color map x number of columns in M (where M is an N_Col x 3 matrix of R G B values (0..1)) return 0
    - If there is a hot spot in the color vector, return 1. Otherwise, return 0
- else ColsContMode = 0
- Create color scale vector
  - Allocate memory to color scale vector
  - Allocate memory to its cv and isMasked components for the number of nodes. BiasCoordVec component nullified until it is determined whether it is needed.
  - If ColsContMode, vCont allocated for the number of nodes
  - if cv or isMasked allocation failed, return NULL
  - Otherwise, assign Nnode (number of nodes) to the output array and return the same.
- Fetch vectors from dataset. Set element to masked if T value within the threshold AND either variable thresholding false or threshold outlining true. The condition is only possible when Opt->ThreshRange[0] > 0
- Setup nodedef so that it can be used along with Sover->V for clusterizing. Sover->V will get modified in subsequent calls so got to do it now
- nd = SUMA_GetNodeDef(dset)
  - ( (!dset || !dset->inel || !dset->inel->vec) ? NULL:(int*)(dset->inel->vec[0]) )
    - IOW get the vector, of 3D color vectors, at the first node of the dataset if it exists. Otherwise return NULL
- Iterate over the vectors that have been filled
  - if (nd)
    - copy nd into Sover→NodeDef
  - Otherwise
    - Fill Sover→NodeDef with 1s
- Sover->FullList = NOPE;
- Colorize
  - SUMA_ScaleToMap
    - Ensure there is an overlay, that it has a name and that a colormap can be built.
    - SUMAg_CF->scm = SUMA_Build_Color_maps();
      - SUMA_Get_AFNI_Default_Color_Maps
        - Initialize N_maps and N_cols to -1. Set pthr[i] = 0.0; pov[i] = 0
        - Cv = SUMA_Add_Color ("none", -1.0, -1.0, -1.0, 1.0, Cv, &N_cols);
          - (r,g,b)==(-1.0,-1.0,-1.0) → “No color”
          - Else return error if (r,g,b) outside [0,1] range
          - Ensure color name not too long. If it is, return with error.
          - Check to see if color exists already. If it does, replace color of that name with new color.
          - Add new colormap.
    - icmap = SUMA_Find_ColorMap (Described above)
    - ColMap = SUMAg_CF→scm→CMv[icmap];
    - Create a scaled color vector
      - if (show mode Con or Cac)
        - if SUMA_NeedsLinearizing(ColMap) (See description above)
          - if (!nwarn)
            - "Cannot do contouring with colormaps that panes of unequal sizes.” "Notice shown once per session."
            - ++nwarn;
            - Opt->ColsContMode = 0;
        - else Opt->ColsContMode = 1;
      - else Opt->ColsContMode = 0;
      - SUMA_Create_ColorScaledVect